## Slide 2
Decouple reaction between carbonate and Benzene(aq), other forms of carbon.
Config →
Redox Couples…
Default setting: all redox reactions are coupled.

## Slide 3
Decoupled redox pairs (Benzene and carbonate) can be constrained independently.
Specify domain’s starting fluid composition on the Initial pane

## Slide 4
add → Kinetic →
Redox reaction
You enable redox kinetics on the Reactants pane.

## Slide 5
Set enzyme function to “on” and enter rate constant, half-saturation constant, and enzyme concentration.
Type out the redox reaction.

## Slide 6
Inlet fluid “contaminated” enters the domain from t = 0 to 2 years
Inlet fluid “flush” enters the domain from t = 2 to 10 years
Define the reaction intervals. Specify what fluids flow into the domain, and when.
Click to add a new reaction interval

## Slide 7
Inlet fluid named “contaminated” carries Benzene into the domain
The various inlet fluids are defined on the Fluids pane
Click to add a new fluid
Click to expand or contract view

## Slide 8
Clean rinse water: negligible Benzene in the “flush” inlet fluid
The various inlet fluids are defined on the Fluids pane

## Slide 9
Specify domain size and gridding on the Domain pane.
Domain is 1 km long, divided into 400 nodal blocks

## Slide 10
Specify flow rate on the Flow pane.
Set specific discharge or hydraulic head/ potential drop
Set a single flowrate for all intervals

## Slide 11
Set various mass transport properties on the Medium pane.
Used to calculate coefficient of hydrodynamic dispersion.
Porosity affects groundwater velocity.
Run → Go
traces the model

## Slide 12
Initial pulse of Benzene contaminated
water is attenuated by biodegradation.