## Slide 2
Aquifer is 70% Quartz
Specify domain’s starting fluid composition on the Initial pane
Initial fluid in equilibrium with Quartz

## Slide 3
add → Kinetic →
Mineral…
Mass already specified on Initial pane
Use Arrhenius equation for polythermal runs
Supply a nucleus density, critical S.I., cross-affinity terms, etc.
You can also…
Add promoting or inhibiting species
Rate constant
Specific surface area
You enable kinetic reactions on the Reactants pane.

## Slide 4
A single inlet fluid flows into the domain for 30 years.
Define the reaction intervals. Specify what fluids flow into the domain, and when.

## Slide 5
SiO2(aq) concentration sets the inlet fluid to be undersaturated with respect to Quartz
The inlet fluid is defined on the Fluids pane

## Slide 6
Domain is 100 m long, divided into 400 nodal blocks
Specify domain size and gridding on the Domain pane.

## Slide 7
Pore fluid in aquifer displaced 100 times over the 30 year timespan we set on the Intervals pane
Specify flowrate on the Flow pane.

## Slide 8
Set various mass transport properties on the Medium pane.
Run → Go
traces the model
No value set, so porosity calculated from volume of equilibrium minerals: 70% Quartz → 30% pore space.

## Slide 9
Inlet fluid is undersaturated with respect to Quartz.
SiO2(aq) concentration approaches Quartz equilibrium value.