## Slide 2
Set the composition of the first fluid on the Basis pane, then equilibrate it.
Fluid 1:
High Ba++, low SO4−−
Run → Go equilibrates the fluid

## Slide 3
Run → Pickup → Reactants → Fluid moves the equilibrated fluid to the Reactants pane and vacates the Basis pane
The Ba++-rich fluid can now be mixed with a new fluid.

## Slide 4
Fluid 2:
Low Ba++, high SO4−−
Set the composition of the second fluid on the vacated Basis pane.

## Slide 5
flash: off → fluid
Run → Go
mixes the fluids
Go to Config → Stepping… to implement a flash model. A flash model mixes two fluids in every possible mixing fraction.

## Slide 6
Fluid 2:
Low Ba++, high SO4−−
Fluid 1:
High Ba++, low SO4−−
Barite does not precipitate from either end-member fluid, but forms extensively in mixture

## Slide 7
Go to Config → Options… to disable mineral precipitation.
Uncheck “precipitation”
Run → Go
mixes the fluids

## Slide 8
Component concentrations demonstrate (semi)conservative mixing behavior when precipitation is disabled.
Fluid 2:
Low Ba++, high SO4−−
Fluid 1:
High Ba++, low SO4−−

## Slide 9
Fluid 2:
Low Ba++, high SO4−−
Fluid 1:
High Ba++, low SO4−−
Barite is undersaturated in end-member fluids, oversaturated in mixture.